## Slide 1: Automotive Communication Protocols
LIN, CAN, Automotive Ethernet
SPI, I2C and UART

## Slide 2: UART – Universal Asynchronous Receiver-Transmitter
Hardware communication protocol
Serial communication with two wires
Most used especially in embedded systems, MCs and computers
Dedicated pins RX – TX
Maximum 1 master and slave
Length of msg: 1 + 9 + 1+ 3 = 14 bits

## Slide 3: SPI - Serial Peripheral Interface
Synchronous
One of the fastest, the downside is that it has 4 wires
Is advantageous when we have 1 master to multiple slaves communication ( but not a rule )
High data transfer rates – exceeding bandwidth of 10 MHz
Length 3 to 16 bits

## Slide 4: I2C : Inter-Integrated Circuit
Combines best features of SPI and UARTs
  Connect multiple slaves to 1 master ( like SPI )
  Synchronous
  Multiple masters controlling one or more salves
  Only 2 wires ( like UART )
SDA(Serial Data) : send data between master and slave
SCL(Serial Clock) : clock signal
100kbps
30 bits length
Project

## Slide 5: LIN – Local Interconnect Network
Single wire - serial network protocol (up to 19 kbps -> 40 meters) in
distributed automotive applications
Cheaper, lower performance and reliability than CAN, but used together. LIN complements CAN
1 master, up to 15 slaves ( 16 nodes)
Collision detection necessary – all comms initiated by master
[break, 13+1][sync, 8][ident, 6+2][data, 8bytes][checksum, 8bit] = aprox 100 bits

## Slide 7: CAN – Controller Area Network
2 wire (twisted-pair) bidirectional serial bus -> allows electronic subsystems to be linked and interact in a network
Designed such that real time information can be exchanged ( transmission, ignition )
Reduced complexity
Symmetric
Massage based rather than address based usually
CSMA/CD
Bit stuffing
Identifier length : 11 to 29 bits
8 bytes of data
1+11+1+6+64+15+1+1+1+7+3 = 111 bits

## Slide 8: More CAN
Differential signaling = two complementary signals Low and High wires
Each message or frame uses digital identifier that provides a message priority arbitration
Exchange rate 1Mbps ( up to 500kbps ) - not sufficient for active safety in modern vehicles
8 bytes of data per single CAN bus message

## Slide 9: CAN-FD ( Flexible Data-Rate )
Broadcast sensor data
64bytes of DATA
Dynamically switch between data rates
Commands reach the output controller much faster

## Slide 10: FelxRay
Successor of CAN
Higher data rates and bigger size
Diff signaling
Time triggered communications – eliminate prioritizing messages
High data rates : 10Mbps
Payload len : 256 bytes
Malfunction on one ECU doesn't impact the rest – they still communicate
High cost compared to CAN

## Slide 11: Automotive Ethernet
Physical layer adapted for automotive use cases
More complex communication -> increased software functionality in cars ( e.g : Autonomous driving ) -> scalability
High bandwidth + higher flexibility -> integration with cloud services
Alternatives to FlexRay and high baud rate versions of CAN
10Base-T1 / 100Base-T1 / 1000Base-T1S -> Mbps
CSMA/CD