## Slide 1: Automotive
Automotive in general
Functional Safety (ISO 26262)
V-Cycle

## Slide 2: Automotive Acronyms
ECU : Electronic Control Unit
OEM : Original Equipment Manufacturer
AES : Automotive Embedded Software
CAN : Controller Area Network
BTS : Bureau of Transportation Statistics
ISO : International Organization for Standardization
ASIL: Automotive Safety Integrity Level framework
HARA : Hazard Analysis and Risk Assessment
ABS : Anti-Breaking System

## Slide 3: Automotive – Auto:Self + Motive:Motion
Differences are made in user experience, autonomous, electric, safety, connectivity rather than traditional vehicle hardware
Automotive embedded software is critical for creating the mobility experience of the future.
Real-time complex interactions across multiple systems : Braking, steering, suspension etc. Each ECU is part of a bigger and complex electrical architecture, sometimes more than 20 interactions in AES apps

## Slide 4: Automotive Industry
6th largest economy
Design – Development – Manufacturing – Repairing of Motor Vehicles
Components: Engines, bodies and not tires, batteries and fuel
Product: Passenger automobiles and light trucks
  Secondary : Commerical vehicles ( semis , delivery trucks etc. )

## Slide 5
More than 10000 electrical devices and 61 micro-processors
Three controller area networks ( CAN )
Several subnetworks
Renault Laguna

## Slide 6: Functional Safety
Automotive functional safety is :
  Implementation of protective measures to eliminate or mitigate hazards
  Hazards: caused by failure or unintended behavior of vehicle-level system
Safety goals are more critical than the functionality of the automotive component
With huge number of ECUs, sensors, actuators, the need to ensure functional safety at every stage of product development and commission has become even more important

## Slide 7: ISO 26262
ISO 26262 standard defines functional safety as the “absence of unreasonable risk due to hazards caused by malfunctioning behavior of electrical/electronic systems”
  Reason for standard :
    Establish various safety requirements -> mitigate risks to acceptable levels
    Smoothly manage and track safety requirements
    Ensure standard safety procedures in delivered products
ASIL (Automotive safety integrity level) : "risk classification scheme for defining the safety requirements"
  Risk parameters : Severity, Exposure and Controllability

## Slide 8: Risk Parameters
Exposure ( E ) : Measure of possibilities of the vehicle being in a hazard or risky situation
E1 – very low probability
E2 .. E3..
E4 - very high probability
Controllability ( C ) : Extent to which control can be established after safety goal breached due to failure or malfunction
C1 – easy; C2..; C3.. ; C4 – most difficult to control
Severity ( S ) : Seriousness of the damage to life of people and property due to safety goal infringement
S1 – light injury, S2 severe and life threatening, S3 life threatening incidences

## Slide 9: ASIL levels:
Classified from D – Highest level of automotive hazard, A – lowest.
QM ( Quality Management level ) Therefore hazards that do not dictate safety requirements
ASIL - A
ASIL - B
ASIL - C
ASIL - D

## Slide 10
Image credit: techdesignforums

## Slide 12: Steps
Definition of the system and its safety-criticality at the vehicular level.
  Hazard Analysis and Risk Assessment ( HARA )
Determine Safety Goals for each component.

## Slide 13: HARA
All scenarios of hazards or dangers evaluated for a particular component
Critical for vehicle safety

## Slide 14: Safety Goals and Issues Types
The level of safety required by an automotive component to function normally without posing any threats to the vehicle.
  Ex: during fire we want the door to open, but during high speed, we want it closed.

## Slide 15: ASIL for ABS - Steps -

## Slide 16: V-Cycle

## Slide 17: Requirements analysis
Purpose :
  Transform software related parts of the system requirements into a set of software requirements
  Describe the WHAT
If the documentation of these requirements is not done, you might overlook or misinterpret customer's expectations which can result in additional costs, delays and effort.

## Slide 18: Base practices ( SR )
Specify software requirements
Structure software requirements
Analyze software requirements: to ensure [correctness, technical feasibility, verifiability]
Analyze impact of operating environment.
Establish bidirectional traceability

## Slide 19: System Requirements
Strong links to SYS.2, and SYS.3 ( upstream )
Strong links to SWE.2 ( architecture – downstream), and SWE.6
Automotive SPICE recommends :
  Consider more than customer requirements
  Regulation, standards, norms, internal requirements
Add stakeholder requirements
Describe the software as a black-box

## Slide 20: Software Architectural Design
Purpose:
  Defines how the functionality will be implemented
  Describe the HOW

## Slide 21: Software Architecture
Develop and Document
Allocate SR
Define interfaces
Behavior
Bidirectional traceability
Communicate the design
Define the right view
Document interfaces accurately
Ensure traceability

## Slide 22: Software Architectural design
Components connected to each other and its shown how functions from either component is used by the other component and other relations
It is visible how each component interfaces with the other components
Traceability supports :
    Consistency checks, impact assessment, reporting of stakeholder expectations

## Slide 23: Detailed Design and Unit Construction
Purpose :
  Basis of the implementation of the code and unit test

## Slide 24: Detailed Design:
Develop detailed design
Define interfaces of SUs
Dynamic behavior
Evaluate design
Bidirectional Traceability
Communicate agreed software detailed design
Develop SUs
ISO 26262 provides guidance in safety critical software
Needs to contain :
Interfaces documentation
  Names
  Types
  Units
  Resolutions
! Should be written before code

## Slide 25: Software Unit Verification
Purpose : Verify software units to provide evidence of compliance of SU with the software detailed design and non-functional SR

## Slide 26: SWE.4 Unit Verification:
Define strategy for SU verification
  Static and dynamic analysis
  Code reviews
  Unit tests
Regression test : make sure that anything that hasn't changed, still works well
Develop criteria for unit verification : MISRA ( standard to ensure code is safe, secure, reliable, portable )
Summary report

## Slide 27: Software Integration and Integration Test
Purpose :
  Integrate SUs into larger software items – consistent with architectural design
  Ensure that software items are tested
  Provide evidence for compliance of integrated SI with architectural design

## Slide 28: SWE.5
Develop software integration strategy
Integrate SUs and SIs
Select test cases
Perform Software integration test
Establish BT
Ensure Consistency
Summarize and communicate results
Integration test strategy
Regression test strategy
Bidirectional Traceability
  For each relevant architectural element, you can localize corresponding test
Consistency :
  Links the subject to the correct test
  Covers subject completely
  No faulty tests
Summary report

## Slide 29: Software Qualification test
Purpose : Ensure that the integrated software is tested to provide evidence for compliance with SR

## Slide 30: Practices :
Develop SQ test strategy and regression test strategy
Develop specification for SQT ( test cases, verification criteria etc.)
Select test cases
Test integrated software
Establish BT ( supports coverage, consistency and impact analysis ).
Ensure Consistency
Summarize and communicate results
Check against the requirements
Close relationship with SWE.1
Clear test strategy
  Test object
  Test methods for test case development
Approach to test automation
Select right test cases
Traceability and consistency ( there are tools for this which also checks consistency)

## Slide 31: Terms
Regression test : for retesting the integrated software if a SI (or component ) is changed
Integrated software : software that is implemented and working to some extend